## Slide 1
QUANDELA · APPLICATION CASE STUDY
I would investigate few-label industrial defect inspection with a photonic reservoir
A measurable 12-week path from public data to a conditional hardware test
NGUYEN NGO NHAT NAM · R&D QUANTUM OPTICS ENGINEER CANDIDATE · 15 SEP 2026 · 15:30 GMT+7
REAL INDUSTRIAL NEED
Scarce expert labels
Quality inspection needs useful accuracy from small labelled sets.
PHOTONIC FIT
Fixed nonlinear map
Interference transforms compact phase-encoded image features.
12-WEEK TEST
Decision-ready result
Public data · matched controls simulator → conditional QPU run
COMPLETED DE-RISKING PILOT
Q1 0.8708
macro-F1 · 48 labels per class
Useful signal; no advantage yet
Evidence informs the next test; it does not support a quantum-advantage claim.
01 / 10
Notes: Good afternoon. I am Nguyen Ngo Nhat Nam. I would investigate few-label industrial defect inspection with a fixed photonic reservoir. Expert labels are costly, interference offers a compact nonlinear map, and the question can be tested in twelve weeks with public data, matched controls, and a simulator-to-hardware path. My completed pilot reached 0.8708 macro-F1 at forty-eight labels per class. That demonstrates useful signal in simulation, not practical or quantum advantage. The choice matters only if the constraint is real and the test is measurable.

## Slide 2
WHY THIS APPLICATION · REAL NEED, MEASURABLE TEST
Why this is a good 12-week feasibility study
Crazing
Inclusion
Patches
Pitted surface
Rolled-in scale
Scratches
REAL NEED
Labels are expensive
The target is useful accuracy from 12 · 24 · 48 labels per class.
Sample efficiency is measurable.
TRACTABLE BENCHMARK
1,800 images
Six balanced defect classes 300 images per class
Public data · macro-F1 target
LEAKAGE-SAFE EVIDENCE
One duplicate group
Pa_101 · Pa_105 never cross splits. Fold 0: 60 test images per class.
Real need · data · decision metric
Source: dataset_audit.csv · frozen experiment protocol
02 / 10
Notes: The operational constraint is label scarcity: inspection images may be plentiful, while reliable labels require expert time. NEU-CLS provides 1,800 audited images across six balanced defect classes, so the study can begin without proprietary collection. The exact duplicate pair Pa_101 and Pa_105 remains in one group, and the pilot test fold has sixty images per class with no overlap. The application therefore has a real need, accessible evidence, and a measurable failure condition. Now I will show where photonics enters.

## Slide 3
WHY QUANDELA · SIMULATOR-TO-HARDWARE PATH
A small reservoir fits Quandela’s path to hardware
FROZEN
OpenCLIP
ViT-B/32 · L2
TRAIN ONLY
PCA-5
phases [−π, π]
6 MODES · 2 PHOTONS
U · D(x) · U
occupation [1,0,1,0,0,0]
fixed U · image-dependent phases
POSTSELECT
21 → 15
conditional P(n|x)
CLASSICAL READOUT
Linear model
macro-F1
1 · PERCEVAL · QUANDELA
Simulation complete
max error 4.16 × 10⁻¹⁷
2 · SECOND IMPLEMENTATION
MerLin cross-check
SEPARATE CODE PATH
NOT EXTERNAL REPLICATION
max error 8.33 × 10⁻¹⁷
3 · REMOTE QPU SUBSET
Proposed next gate
NOT YET EXECUTED
Official docs: perceval.quandela.net/docs/v1.2 · merlinquantum.ai/0.4 · local verification.json
03 / 10
Notes: A frozen OpenCLIP encoder produces an embedding. Train-only principal component analysis reduces it to five phase values. A fixed six-mode, two-photon circuit maps them to fifteen postselected probabilities for a linear readout. Only the readout is trained, which isolates the feature map. Perceval is the primary simulation path; MerLin reproduces the ideal probabilities to machine precision through a separate code path, not external replication. Remote QPU execution remains untested and conditional on access and prior gates. A runnable simulation is only a starting point, so I need a rule that can reject it.

## Slide 4
FEASIBILITY QUESTION · PREDEFINED DECISION
The feasibility question is deliberately falsifiable
AT THE SAME PCA-5 INPUT
Can Q1’s 15-D photonic features beat matched 15-D controls and approach PCA-5 RBF-SVM?
PAIRED PROTOCOL
12 · 24 · 48
labels per class
Subset seeds 11 · 22 · 33 Map seeds 101 · 202 · 303 Validation macro-F1 only One test evaluation per selected fitted pipeline
MAP SEEDS AVERAGED · NEVER PICKED
7 FAMILIES · EQUAL-WIDTH SCHEMATIC
B1 Full CLIP + linear
B2 Full CLIP + RBF-SVM
B3 PCA-5 + linear
B4 PCA-5 + RBF-SVM
B5 RFF-15
B6 ELM-15
Q1 Photonic-15
PASS A · ACCURACY PARITY
Q1@48 ≥ B4@48 − 0.02
on at least 4 / 5 outer folds
PASS B · 2× LABEL EFFICIENCY
Q1@24 ≥ B4@48 − 0.02
≥4 / 5 folds · ≤2,000 shots / image
acceptance rate ≥ 0.70
STOP IF NEITHER PASS HOLDS
or Q1 loses to RFF-15 and ELM-15 on ≥4 / 5 folds
Matched 15-D controls: Random Fourier Features (RFF) and Extreme Learning Machine (ELM).
B4 = PCA-5 radial-basis-function support vector machine (RBF-SVM); resource value = label efficiency under shot and acceptance constraints.
04 / 10
Notes: From the same PCA-five input, can Q1 beat matched fifteen-dimensional controls and approach B4, the PCA-five RBF-SVM? RFF means random Fourier features; ELM means extreme learning machine. I preregister two pass routes. Pass A: at forty-eight labels per class, Q1 is within 0.02 macro-F1 of B4 on at least four of five folds. Pass B: Q1 at twenty-four labels reaches B4 at forty-eight labels within 0.02 on four folds, using at most two thousand shots per image and acceptance of at least 0.70. I stop if neither passes, or Q1 loses to both RFF-15 and ELM-15 on four folds. These gates define the proposed project; the pilot is already complete.

## Slide 5
APPROACH · COMPLETED PILOT → PROPOSED PROJECT
The 12-week project starts after the completed pilot
PRE-STUDY · COMPLETED PILOT
Data audit · frozen protocol · simulator verification · fold-0 result
1–2
3–4
5–6
7–8
9–10
11–12
REPLICATE
Five-fold replication
DELIVERABLE
Fold-level table
EXIT
Ranking stable across folds
ABLATE
PCA · circuit
measurement
DELIVERABLE
Ablation matrix
EXIT
Candidate beats matched controls
NOISE
Loss · drift detectors
DELIVERABLE
Robustness curves
EXIT
No collapse under credible noise
FREEZE
Hardware candidate
DELIVERABLE
Frozen run spec
EXIT
Shots · calibration metadata locked
QPU GATE
Remote subset raw counts
DELIVERABLE
Calibrated result
EXIT
Run only after prior gates pass
DECIDE
Harder-data or independent replication
DELIVERABLE
Decision memo
EXIT
Utility evidence or disciplined stop
The 12-week clock begins with five-fold replication—not work already completed.
05 / 10
Notes: The pilot is pre-study evidence and does not consume the project clock. Weeks one and two replicate five outer folds. Weeks three and four ablate PCA, circuit, and measurement choices. Weeks five and six add realistic photonic noise. Weeks seven and eight freeze one hardware candidate and its resource definitions. Weeks nine and ten run a remote subset only if prior gates pass. Weeks eleven and twelve use harder data or independent replication and produce the decision memo. Here is what the pilot actually found.

## Slide 6
COMPLETED PILOT · PRIMARY EVIDENCE
The pilot shows useful signal—not competitive advantage
Q1 · PHOTONIC-15
0.7812 → 0.7886
→ 0.8708
12 · 24 · 48 labels per class
B1 · FULL CLIP + LINEAR
0.9242 → 0.9638
→ 0.9852
PILOT VERDICT
Learns signal; not competitive yet.
Mean ± sample SD across three subset seeds · one outer fold · source: main_results.csv
06 / 10
Notes: Q1 rises from 0.7812 to 0.7886 and then 0.8708 as the label budget grows. The full OpenCLIP linear baseline starts at 0.9242 and reaches 0.9852. Each point averages three subset seeds, but every point reuses one outer test fold. The correct conclusion is limited: Q1 contains useful class information in this simulation pilot, while the current map is not competitive with the full representation. The controlled comparison shows where that gap comes from.

## Slide 7
DIAGNOSIS · REPRESENTATION AND CONTROLS
PCA-5 explains most of the gap; the map explains the rest
FULL → PCA-5 PENALTY · B1 − B3
+.1018 · +.0993 · +.0713
budgets 12 · 24 · 48
Q1 − RFF
+.3133 · +.2238 · +.2307
Q1 − ELM
−.0166 · −.0432 · −.0215
Q1 − PCA-5 RBF-SVM
−.0507 · −.0558 · −.0534
Only win: locked matched RFF-15 comparator.
Separate information lost in PCA-5 from the value added by the photonic circuit.
Source: compression.csv · paired_differences.csv · subset-paired descriptive differences
07 / 10
Notes: PCA-five costs the linear baseline about 0.07 to 0.10 macro-F1, accounting for most of the gap to the full representation. Within the compressed setting, Q1 beats the locked RFF-15 comparator by 0.22 to 0.31. It still trails ELM by about 0.02 to 0.04 and PCA-five RBF-SVM by about 0.05 to 0.06, so map choice explains the remaining shortfall. I would therefore vary representation size and circuit design separately. Before proposing hardware, I also tested whether sampling is stable.

## Slide 8
STRESS TEST · FINITE-SHOT FEASIBILITY
Finite-shot sampling is stable; accuracy does not recover
Q1 · 24 LABELS / CLASS · OUTER FOLD 0
MACRO-F1
ACCEPTANCE RATE
MACRO-F1 · 15 EVALUATIONS EACH
500
0.7662 ± .0322
2,000
0.7739 ± .0308
8,000
0.7725 ± .0363
acceptance ≈ 0.754
0 zero-acceptance failures
TESTED
Shot sampling Acceptance Ideal-trained readout
NOT YET TESTED
Loss · phase drift Distinguishability Detectors · noise training
45 evaluations = 3 map seeds × 5 sampling seeds × 3 shot levels · same outer test fold · source: finite_shot.csv
08 / 10
Notes: At twenty-four labels per class on outer fold zero, Q1 stays near 0.77 from five hundred to eight thousand shots. Each level has three map seeds by five sampling seeds; all forty-five evaluations share that fold. Acceptance is near 0.754 with no failures. Increasing shots does not recover accuracy, so sampling noise is not the main limitation in this range. Loss, drift, distinguishability, detector effects, and noise-aware training remain untested. These results define the evidence boundary.

## Slide 9
CURRENT VERDICT · EVIDENCE BOUNDARY
Simulation pipeline demonstrated; hardware feasibility untested
DEMONSTRATED
Simulation pipeline
Executable pipeline Simulator consistency Reproducible artifacts
PARTIALLY ANSWERED
Application signal
Learning with labels Paired one-fold ranking Finite-shot sampling
UNANSWERED
Practical utility
Five-fold generalization Realistic photonic noise Remote hardware execution
OPENCLIP EMBEDDINGS · CPU
96.57 s
One cached feature pass
Reused across every model family.
PILOT MODEL GRID · CPU
≈59.9 s
Broader validation is tractable
Five folds fit the project window.
DECISION CONSTRAINT
Scientific validity
One outer fold · small validation cells ideal optics · B1 near ceiling
RUNTIME IS NOT THE BOTTLENECK
Local CPU profile · no loss, phase drift, detector noise, or QPU queue
09 / 10
Notes: The demonstrated result is simulation-pipeline feasibility: the code executes, two implementation paths agree, and the artifacts are reproducible. Application signal is only partly answered because the ranking comes from one outer fold. Hardware feasibility remains untested because realistic noise and remote execution are unfinished. Local computation is not the bottleneck: embedding extraction took 96.57 seconds and the pilot model grid about 59.9 seconds. The bottleneck is scientific validity across folds, noise, and calibrated hardware. That boundary leads to a conditional recommendation.

## Slide 10
RECOMMENDATION · ANSWER TO THE RESEARCH TEAM
Continue only through a decision-changing test
WHICH APPLICATION?
Few-label industrial defect inspection
with a fixed photonic reservoir
WHY THIS IDEA?
Real label scarcity · compact phase encoding
Quandela simulator → hardware path · 12-week evidence
CURRENT VERDICT
Feasible in simulation and scientifically interesting
HARDWARE FEASIBILITY REMAINS UNTESTED
CONTINUE ONLY IF · B4 = PCA-5 RBF-SVM
PASS A · Q1@48 ≥ B4@48 − 0.02
↳ on ≥4 / 5 folds
PASS B · Q1@24 ≥ B4@48 − 0.02
↳ on ≥4 / 5 folds · ≤2,000 shots / image
↳ acceptance ≥ 0.70
STOP CONDITION
Neither pass holds
or Q1 loses to RFF-15 and ELM-15 on ≥4 / 5 folds.
Evidence first · hardware only after gates pass
Repository · github.com/MonsieurNam/Quanova_Photonic_Defect_QML
10 / 10
Notes: My recommendation is conditional. Few-label defect inspection fits a useful Quandela simulator-to-hardware study, and the pilot shows that the simulation workflow is executable. It has not demonstrated practical or hardware advantage. B4 is the PCA-five RBF-SVM reference. I continue only if Pass A at forty-eight labels or Pass B for twofold label efficiency holds. The shot and acceptance constraints belong only to Pass B. If neither passes, or Q1 loses to RFF-15 and ELM-15 on at least four folds, I report simulation feasibility without utility and stop before spending QPU time. Thank you.