## Slide 1
QUANDELA · APPLICATION CASE STUDY
I would investigate few-label industrial defect inspection with a photonic reservoir
A measurable 12-week path from public data to a conditional hardware test
NGUYEN NGO NHAT NAM · R&D QUANTUM OPTICS ENGINEER CANDIDATE · 15 SEP 2026 · 15:30 GMT+7
REAL INDUSTRIAL NEED
Scarce expert labels
Quality inspection needs useful accuracy from small labelled sets.
PHOTONIC FIT
Fixed nonlinear map
Interference transforms compact phase-encoded image features.
12-WEEK TEST
Decision-ready result
Public data · matched controls simulator → conditional QPU run
COMPLETED DE-RISKING PILOT
Q1 0.8708
macro-F1 · 48 labels per class
Useful signal; no advantage yet
Evidence informs the next test; it does not support a quantum-advantage claim.
01 / 10
Notes: Good afternoon. I am Nguyen Ngo Nhat Nam, and I would investigate few-label industrial defect inspection using a fixed photonic reservoir. I chose it for three reasons: expert defect labels are costly, photonic interference offers a compact nonlinear feature map, and the idea can be evaluated rigorously within twelve weeks using public data, matched controls, and a staged path from simulation to hardware. I have already completed a de-risking pilot. Q1 reached 0.8708 macro-F1 at forty-eight labels per class. That is useful signal, but it is not evidence of practical or quantum advantage.

## Slide 2
WHY THIS APPLICATION · REAL NEED, MEASURABLE TEST
Why this is a good 12-week feasibility study
Crazing
Inclusion
Patches
Pitted surface
Rolled-in scale
Scratches
REAL NEED
Labels are expensive
The target is useful accuracy from 12 · 24 · 48 labels per class.
Sample efficiency is measurable.
TRACTABLE BENCHMARK
1,800 images
Six balanced defect classes 300 images per class
Public data · macro-F1 target
LEAKAGE-SAFE EVIDENCE
One duplicate group
Pa_101 · Pa_105 never cross splits. Fold 0: 60 test images per class.
Real need · data · decision metric
Source: dataset_audit.csv · frozen experiment protocol
02 / 10
Notes: The operational constraint is label scarcity. Inspection images may be plentiful, but reliable defect labels consume expert time. Performance at twelve, twenty-four, and forty-eight labels per class is therefore a meaningful target. NEU-CLS gives 1,800 audited images across six balanced steel-surface defect classes, so the study can start without waiting for proprietary data. The evaluation also has a clear failure mode: the exact duplicate pair Pa_101 and Pa_105 remains in one group, and the pilot test fold contains sixty images per class with no sample or duplicate-group overlap. This gives a real need, accessible evidence, and a quantitative decision.

## Slide 3
WHY QUANDELA · SIMULATOR-TO-HARDWARE PATH
A small reservoir fits Quandela’s path to hardware
FROZEN
OpenCLIP
ViT-B/32 · L2
TRAIN ONLY
PCA-5
phases [−π, π]
6 MODES · 2 PHOTONS
U · D(x) · U
occupation [1,0,1,0,0,0]
fixed U · image-dependent phases
POSTSELECT
21 → 15
conditional P(n|x)
CLASSICAL READOUT
Linear model
macro-F1
1 · PERCEVAL · QUANDELA
Simulation complete
max error 4.16 × 10⁻¹⁷
2 · SECOND IMPLEMENTATION
MerLin cross-check
SEPARATE CODE PATH
NOT EXTERNAL REPLICATION
max error 8.33 × 10⁻¹⁷
3 · REMOTE QPU SUBSET
Proposed next gate
NOT YET EXECUTED
Official docs: perceval.quandela.net/docs/v1.2 · merlinquantum.ai/0.4 · local verification.json
03 / 10
Notes: The architecture is deliberately hybrid and small. A frozen OpenCLIP encoder produces an image embedding. Principal component analysis is fitted on training data only and reduces it to five values scaled from minus pi to pi. Those phases enter a fixed six-mode, two-photon circuit. Postselection turns twenty-one possible outcomes into fifteen conditional probabilities for a linear readout. Only the readout is trained, which isolates the feature map and avoids a costly variational loop. Perceval is the primary simulation layer. A second implementation in MerLin reproduces the probabilities to machine precision. That is a separate code path inside the same ecosystem, not external replication. Both checks are complete. Remote QPU execution remains a proposed final gate, subject to access.

## Slide 4
FEASIBILITY QUESTION · PREDEFINED DECISION
The feasibility question is deliberately falsifiable
AT THE SAME PCA-5 INPUT
Can Q1’s 15-D photonic features beat matched 15-D controls and approach PCA-5 RBF-SVM?
PAIRED PROTOCOL
12 · 24 · 48
labels per class
Subset seeds 11 · 22 · 33 Map seeds 101 · 202 · 303 Validation macro-F1 only One test evaluation per selected fitted pipeline
MAP SEEDS AVERAGED · NEVER PICKED
7 FAMILIES · EQUAL-WIDTH SCHEMATIC
B1 Full CLIP + linear
B2 Full CLIP + RBF-SVM
B3 PCA-5 + linear
B4 PCA-5 + RBF-SVM
B5 RFF-15
B6 ELM-15
Q1 Photonic-15
PASS A · ACCURACY PARITY
Q1 ≥ RBF-SVM − 0.02
on at least 4 / 5 outer folds
PASS B · 2× LABEL EFFICIENCY
Q1@24 ≥ RBF-SVM@48 − 0.02
≥4 / 5 folds · ≤2,000 shots / image
acceptance rate ≥ 0.70
STOP IF NEITHER PASS HOLDS
or Q1 fails both matched controls on ≥4 / 5 folds
Matched 15-D controls: Random Fourier Features (RFF) and Extreme Learning Machine (ELM).
RBF-SVM = radial-basis-function support vector machine. Resource value is pre-specified as label efficiency under shot and acceptance constraints.
04 / 10
Notes: The question is specific: from the same PCA-five input, can Q1’s fifteen-dimensional photonic features beat matched fifteen-dimensional controls and approach PCA-five RBF-SVM? RFF means random Fourier features; ELM means extreme learning machine; and RBF-SVM means radial-basis-function support vector machine. The protocol uses nested label budgets, validation-only selection, averaged map seeds, and one test evaluation per selected fitted pipeline. I would preregister two pass routes. Accuracy passes if Q1 is within 0.02 macro-F1 of PCA-five RBF-SVM on at least four of five outer folds. Resource value passes if Q1 with twenty-four labels per class reaches the forty-eight-label RBF-SVM within 0.02 on at least four folds, using at most two thousand launched shots per image and an acceptance rate of at least 0.70. If neither route passes, or Q1 fails both matched controls on at least four folds, I stop.

## Slide 5
APPROACH · COMPLETED PILOT → PROPOSED PROJECT
The 12-week project starts after the completed pilot
PRE-STUDY · COMPLETED PILOT
Data audit · frozen protocol · simulator verification · fold-0 result
1–2
3–4
5–6
7–8
9–10
11–12
REPLICATE
Five-fold replication
DELIVERABLE
Fold-level table
EXIT
Ranking stable across folds
ABLATE
PCA · circuit
measurement
DELIVERABLE
Ablation matrix
EXIT
Candidate beats matched controls
NOISE
Loss · drift detectors
DELIVERABLE
Robustness curves
EXIT
No collapse under credible noise
FREEZE
Hardware candidate
DELIVERABLE
Frozen run spec
EXIT
Shots · calibration metadata locked
QPU GATE
Remote subset raw counts
DELIVERABLE
Calibrated result
EXIT
Run only after prior gates pass
DECIDE
Harder data replication
DELIVERABLE
Decision memo
EXIT
Utility evidence or disciplined stop
The 12-week clock begins with five-fold replication—not work already completed.
05 / 10
Notes: The pilot is pre-study evidence; it does not consume the twelve-week project. The dataset audit, frozen protocol, simulator checks, finite-shot test, and fold-zero result are complete. Weeks one and two replicate all five outer folds. Weeks three and four ablate PCA dimension, circuit design, and measurement choices. Weeks five and six add loss, phase drift, partial distinguishability, detector effects, and noise-aware training. Weeks seven and eight select and freeze one hardware candidate, including preprocessing, shot definition, and calibration fields. Weeks nine and ten run a remote QPU subset only if the earlier gates pass. Weeks eleven and twelve use harder data or an independent evaluation, account for resources, and produce a go-or-stop memo.

## Slide 6
COMPLETED PILOT · PRIMARY EVIDENCE
The pilot shows useful signal—not competitive advantage
Q1 · PHOTONIC-15
0.7812 → 0.7886
→ 0.8708
12 · 24 · 48 labels per class
B1 · FULL CLIP + LINEAR
0.9242 → 0.9638
→ 0.9852
PILOT VERDICT
Learns signal; not competitive yet.
Mean ± sample SD across three subset seeds · one outer fold · source: main_results.csv
06 / 10
Notes: Here is the primary pilot evidence. Q1 rises from 0.7812 at twelve labels per class to 0.7886 at twenty-four and 0.8708 at forty-eight. The upward trend shows that the photonic features contain class information. The full OpenCLIP linear baseline, however, starts at 0.9242 and reaches 0.9852. Each point averages three subset seeds, with sample-standard-deviation error bars, but all points reuse one outer test fold. The correct conclusion is that Q1 learns useful structure on this pilot while the current configuration does not justify replacing the full embedding or claiming an advantage.

## Slide 7
DIAGNOSIS · REPRESENTATION AND CONTROLS
Compression—not photonics alone—explains the shortfall
FULL → PCA-5 PENALTY · B1 − B3
+.1018 · +.0993 · +.0713
budgets 12 · 24 · 48
Q1 − RFF
+.3133 · +.2238 · +.2307
Q1 − ELM
−.0166 · −.0432 · −.0215
Q1 − PCA-5 RBF-SVM
−.0507 · −.0558 · −.0534
Only win: locked matched RFF-15 comparator.
Separate information lost in PCA-5 from the value added by the photonic circuit.
Source: compression.csv · paired_differences.csv · subset-paired descriptive differences
07 / 10
Notes: The diagnosis changes the next experiment. Compressing the full embedding to five principal components costs the linear baseline about 0.07 to 0.10 macro-F1, so information is lost before the nonlinear map is tested. Within the compressed comparison, Q1 beats the locked RFF-fifteen comparator by about 0.22 to 0.31. It still trails ELM by roughly 0.02 to 0.04 and PCA-five RBF-SVM by about 0.05 to 0.06. The surviving claim is narrow: this photonic map is better than one matched random-feature control, but not the stronger nonlinear controls. I would therefore vary representation size and circuit design separately.

## Slide 8
STRESS TEST · FINITE-SHOT FEASIBILITY
Finite-shot sampling is stable; accuracy does not recover
MACRO-F1
ACCEPTANCE RATE
MACRO-F1 · 15 EVALUATIONS EACH
500
0.7662 ± .0322
2,000
0.7739 ± .0308
8,000
0.7725 ± .0363
acceptance ≈ 0.754
0 zero-acceptance failures
TESTED
Shot sampling Acceptance Ideal-trained readout
NOT YET TESTED
Loss · phase drift Distinguishability Detectors · noise training
45 evaluations = 3 map seeds × 5 sampling seeds × 3 shot levels · same outer test fold · source: finite_shot.csv
08 / 10
Notes: The finite-shot test asks whether sampled probabilities are stable enough for a later hardware comparison. Macro-F1 is 0.7662 at five hundred launched shots, 0.7739 at two thousand, and 0.7725 at eight thousand. Each shot level contains fifteen evaluations: three map seeds times five sampling seeds. Across all three levels, that is forty-five evaluations on the same outer test fold. Acceptance stays near 0.754, with no zero-acceptance failure. More shots do not recover accuracy monotonically, so shot count alone does not close the gap. This tests sampling around an ideal-trained readout; loss, drift, distinguishability, detectors, and noise-aware training remain future work.

## Slide 9
CURRENT VERDICT · EVIDENCE BOUNDARY
Technically feasible; practical utility remains open
PROVEN
Technical feasibility
Executable pipeline Simulator semantics Reproducible artifacts
PARTIALLY ANSWERED
Application signal
Learning with labels Paired one-fold ranking Finite-shot sampling
UNANSWERED
Practical utility
Five-fold generalization Realistic photonic noise Remote hardware execution
OPENCLIP EMBEDDINGS · CPU
96.57 s
One cached feature pass
Reused across every model family.
PILOT MODEL GRID · CPU
≈59.9 s
Broader validation is tractable
Five folds fit the project window.
DECISION CONSTRAINT
Scientific validity
One outer fold · small validation cells ideal optics · B1 near ceiling
RUNTIME IS NOT THE BOTTLENECK
Local CPU profile · no loss, phase drift, detector noise, or QPU queue
09 / 10
Notes: The evidence supports a three-level verdict. Technical feasibility is proven: the pipeline executes, two implementations agree, and the artifacts are reproducible. Application signal is partly answered: Q1 improves with labels, the paired one-fold ranking is known, and finite-shot sampling is stable in the tested range. Practical utility remains open because five-fold generalization, realistic noise, and remote hardware are unfinished. Local runtime is not the constraint: cached OpenCLIP extraction took 96.57 seconds, and the pilot model grid took about 59.9 seconds on CPU. The bottleneck is scientific validity under more folds, stronger controls, realistic noise, and calibrated hardware.

## Slide 10
RECOMMENDATION · ANSWER TO THE RESEARCH TEAM
Continue only through a decision-changing test
WHICH APPLICATION?
Few-label industrial defect inspection
with a fixed photonic reservoir
WHY THIS IDEA?
Real label scarcity · compact phase encoding
measurable evidence within 12 weeks
CURRENT VERDICT
Technically feasible and scientifically interesting
NO DEMONSTRATED PRACTICAL ADVANTAGE YET
CONTINUE ONLY IF
Pass A · gap ≤ 0.02 on ≥4 / 5 folds
or Pass B · 2× label efficiency
≤2,000 shots / image · acceptance ≥ 0.70
STOP CONDITION
Neither pass holds
or matched controls win on ≥4 / 5 folds.
Evidence first · hardware only after gates pass
Repository · github.com/MonsieurNam/Quanova_Photonic_Defect_QML
10 / 10
Notes: My recommendation is to continue this application only through a decision-changing test. The case is worth testing because label scarcity is real, the compact circuit fits Quandela’s simulator-to-hardware path, and the pilot proves that the workflow can be executed. It has not yet demonstrated practical advantage. I would continue only if the preregistered accuracy-parity or label-efficiency gate passes. If Q1 still beats only RFF while ELM and RBF-SVM remain stronger, I would report technical feasibility without utility and stop. The repository link contains the protocol, implementation, results, and presentation artifacts needed to audit that decision. Thank you.